## Slide 1: Computer Networks CS 3001 (BCS-5B) Lecture 1
Danyal Farhat
FAST School of Computing
NUCES Lahore

## Slide 2
Chapter 1 Introduction
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020

## Slide 3: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Protocol layers, service models

## Slide 4: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 5: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 6: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 7: Caravan analogy
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka link)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth
(aka link)
toll booth
Notes: Here “service” is equivalent to transmission delay.
While nodal processing and queuing delays did not consider.

## Slide 8: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 mins, first car arrives at second booth; three cars still at first booth

## Slide 9: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 10: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 11: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
Traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link

## Slide 12: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 13: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 14: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 15: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 16: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Protocol layers, service models

## Slide 17: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question: is there any hope of organizing structure of network?
and/or our discussion of networks?

## Slide 18: Example: organization of air travel
a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
How would you define/discuss the system of airline travel?
end-to-end transfer of person plus baggage

## Slide 19: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 20: Why layering?
Approach to designing/discussing complex systems:
explicit structure allows identification, relationship of system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 21: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical
Notes: Ethernet has many physical-layer protocols: one for twisted-pair copper wire, another for coaxial cable, another for fiber, and so on. In each case, a bit is moved across the link in a different way.

## Slide 22: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 23: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 24: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 25: Encapsulation
message
segment
datagram
frame
Matryoshka dolls (stacking dolls)
Credit: https://dribbble.com/shots/7182188-Babushka-Boi
Notes: Thanks to Nikko Bovornkeeratiroj, Phuthipong <phuthipong@cs.umass.edu>, for the stacking dolls idea and slides

## Slide 26: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
M
message
Ht
M
segment
M
Ht
Hn
datagram
frame
M
Ht
Hn
Hl

## Slide 27: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 28: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 29: Additional Chapter 1 slides

## Slide 30: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model

## Slide 31: Wireshark
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 32: Thank You!