## Slide 1: Computer Networks CS 3001 (BCS-5B) Lecture 2
Danyal Farhat
FAST School of Computing
NUCES Lahore

## Slide 2
Chapter 2 Application Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top-Down Approach 8th edition n Jim Kurose, Keith Ross Pearson, 2020

## Slide 3: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS

## Slide 4: E-mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 5: E-mail: mail servers
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
client: sending mail server
“server”: receiving mail server
Notes: When a mail server sends mail to other mail servers, it acts as an SMTP client.
When a mail server receives mail from other mail servers, it acts as an SMTP server.

## Slide 6: SMTP RFC (5321)
uses TCP to reliably transfer email message from client (mail server initiating connection) to server, port 25
  direct transfer: sending server (acting like client) to receiving server
three phases of transfer
  SMTP handshaking (greeting)
  SMTP transfer of messages
  SMTP closure
command/response interaction (like HTTP)
  commands: ASCII text
  response: status code and phrase
initiate TCP
connection
RTT
time
220
250 Hello
HELO
SMTP handshaking
TCP connection
initiated
“client”
SMTP server
“server”
SMTP server
SMTP transfers

## Slide 7: Scenario: Alice sends e-mail to Bob
1) Alice uses UA to compose e-mail message “to” bob@someschool.edu
4) SMTP client sends Alice’s message over the TCP connection
user
agent
mail
server
mail
server
1
2
3
4
5
6
Alice’s mail server
Bob’s mail server
user
agent
2) Alice’s UA sends message to her mail server using SMTP; message placed in message queue
3) client side of SMTP at mail server opens TCP connection with Bob’s mail server
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message

## Slide 8: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection

## Slide 9: SMTP: observations
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: client pull
SMTP: client push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response message
SMTP: multiple objects sent in multipart message

## Slide 10: Mail message format
SMTP: protocol for exchanging e-mail messages, defined in RFC 5321 (like RFC 7231 defines HTTP)
RFC 2822 defines syntax for e-mail message itself (like HTML defines syntax for web documents)
header
body
blank
line
header lines, e.g.,
  To:
  From:
  Subject:
  these lines, within the body of the email message area different from SMTP MAIL FROM:, RCPT TO: commands!
Body: the “message” , ASCII characters only

## Slide 11: Retrieving email: mail access protocols
sender’s e-mail
server
SMTP
SMTP
receiver’s e-mail
server
e-mail access
protocol
(e.g., IMAP, HTTP)
user
agent
user
agent
SMTP: delivery/storage of e-mail messages to receiver’s server
mail access protocol: retrieval from server
  IMAP: Internet Mail Access Protocol [RFC 3501]: messages stored on server, IMAP provides retrieval, deletion, folders of stored messages on server
HTTP: gmail, Hotmail, Yahoo!Mail, etc. provides web-based interface on top of STMP (to send), IMAP (or POP) to retrieve e-mail messages

## Slide 12: Thank You!